## Slide 1: V-REP 入门简介
virtuel robot experimentation platform
This presentation is inspired by the official V-REP presentation and the official website

## Slide 2: Content
V-REP 概述
Scene Objects（场景物体）
Ca lcula tion Modules（计算模块）
Control Mechanis ms（控制机制）

## Slide 3: V-REP Overview
What is it?
General purpose robot s im ula tor with integra ted developm ent environment

## Slide 4: V-REP Overview
What is it?
What can it do ?
General purpose robot s im ula tor with integra ted developm ent environment
Sensors, mechanisms, robots and whole s ys tems can be modelled and s im ula ted in various ways

## Slide 5: V-REP Overview
What is it?
What can it do ?
Typical applications ?
General purpose robot s im ula tor with integra ted developm ent environment
Sensors, mechanisms, robots and whole s ys tems can be modelled and s im ula ted in various ways
Fast prototyping and verifica tion Controller development
Hardware control
Simulation of factory automation systems Safety monitoring
Product presentation etc.

## Slide 6: Three Central Elements
Scene Objects
Control
Mechanis ms
Calculation Modules

## Slide 7: Scene Objects
Bas ic building blocks
14 different types
Can be combined with each other
Can form complex systems together with ca lcula tion modules and control
mechanis ms
Scene Objects
Control
Mechanisms
Ca lcula tion
Modules

## Slide 8: Scene Objects
Scene Objects

## Slide 9: Shapes and Dummies
Shapes
Random mesh, convex mesh, primitive mesh, or heightfield mesh Can be grouped/ ungrouped (also merged)
Optim ized for fas t ca lcula tions
Dummies
Auxilia ry reference frame & helper object

## Slide 10: Joints and Force/ Torque Sensors
Joints
Revolute-type • Pris matic -type • Screw-type • Spherical-type Velocity, pos ition, spring/ damper or force controlled
Behavior is controlled by phys ica l engine Easy to do inverse kinematics
Force/ Torque Sensors
Measures force and torque Can conditiona lly break apart
Us ed to ‘glue’ rigid parts together
(not as s trong as grouping, but keeps individua l dynamics )

## Slide 11: Cameras, Lights, and Mirrors
Cameras
Perspective / orthographic projection Tracking & automatic view-fitting
function
Lights
Spotlight / directiona l / omnidirectiona l
Mirrors
Mirror or scene / object clipping function

## Slide 12: Cameras, Lights, and Mirrors

## Slide 13: Proximity Sensors
More than s im ple ray-type detection Configura ble detection volum e
Can be used to model almost any type of proxim ity sensor, from ultrasonic to infrared, and so on.

## Slide 14: Graphs
Time graphs • X/ Y graphs • 3D curves • Can be exported
Us eful debugging tool!

## Slide 15
Vision Sensors
Integra ted image processing • Ray-tra ced rendering a ls o ava ila ble

## Slide 16: Paths and Mills
Paths
6 dim . tra jectory definition Generate a path from the edge
of a shape.
Mills
Custom iza ble cutting volum e Cuts shapes (i.e. meshes)

## Slide 17: Octrees and Point Clouds
Point Clouds
Point container

## Slide 18: Calculation modules
5 bas ic a lgorithm s
Can be combined with each other
Scene Objects
Control
Mechanisms
Ca lcula tion
Modules

## Slide 19: Calculation modules
Ca lcula tion
Modules

## Slide 20: Inverse/ forward kinematics & Minimum Distance Calculations
Inverse/ forward kinematics
Any mechanism: redundant, branched, clos ed, etc.
Da mped / undamped resolution
Weighted resolution • Conditiona l resolution Obstacle a voidance
Minimum Distance Calculations Any mesh • Any point cloud • Any individua l point

## Slide 21: Collision Detection and Path Planning
Collision Detection
Any mesh • Any point cloud • Any individual point
Path Planning
Planning tasks in 3D- space, and in 2D-s pace for vehic les with non-
holonom ic motion constraints.

## Slide 22: Collision Detection and Path Planning
Collision Detection
Any mesh • Any point cloud • Any individual point
Path Planning
Planning tasks in 3D- space, and in 2D-s pace for vehic les with non-
holonom ic motion constraints.

## Slide 23: Dynamics / Physics
4 physics engines:
Bullet Phys ics
Open Dyna mics Engine (ODE)
Vortex Dyna mics
Newton Dyna mics
Sim ple switching
Dyna m ic partic les to s im ula te a ir or water jets

## Slide 24: Dynamics
Static/ non-s tatic shapes
respondable/ non-res pondable shapes (masks)

## Slide 25: Control Mechanisms
6 methods or interfaces
7 languages
All methods can be used at the same time, and even work hand-in-ha nd
Scene Objects
Control
Mechanisms
Ca lcula tion
Modules

## Slide 26: Control Mechanisms
Control
Mechanis ms
Embedded Scripts
Remote API clients
Plugins
ROS nodes
Add-ons

## Slide 27: Control Mechanisms
Embedded Scripts
Plugins
Add-ons
Remote Interface Different process / hardware
Local Interface
Same process
Remote API clients
ROS nodes

## Slide 28: Control Mechanisms
Embedded Scripts
Plugins
Add-ons
Over 500 API functions
(Extenda ble)
Can be attached to any scene object Many Lua extens ion libra ries ava ila ble
Threaded or non-threa ded
Va rious types: ma in script, child scripts , ca llba ck scripts
(e.g. custom joint controllers)
Lua interface
Lightweight and easy to program (child scripts )
→ Initialization • Actua tion • Sensing • shut down
Extremely portable solution

## Slide 29: Control Mechanisms
Embedded Scripts
Plugins
Add-ons
Non-threa ded child script

## Slide 30: Control Mechanisms
Embedded Scripts
Plugins
Add-ons
Over 500 API functions. Extendable C/ C++ interface
Us ed to provide V-REP with a special functiona lity requiring
either fast ca lculation capability (s cripts are most of the tim e s lower than compiled languages), a specific interface to a hardware device (e.g. a real robot), or a special communication interface with the outside world
The ROS functiona lity is pla ced in a plugin

## Slide 31: Control Mechanisms
Embedded Scripts
Plugins
Add-ons
Over 400 API functions. Extendable Lua interface
Can customize the s imula tor Lightweight and easy to set-up
Can s tart automatically and run in the background, or they can be called as functions

## Slide 32: Control Mechanisms
Remote API clients
ROS nodes
Over 100 API functions
(Extendable)
Client (your program) - Server (v-rep plugin) relationship
C/ C++, Python, Java, Matlab, Octave, Lua & Urbi interfaces Lightweight and easy to use
Python Example

## Slide 33: Control Mechanisms
Remote API clients
ROS nodes
Plugin-based
It acts as a ROS node that other nodes can communicate with via ROS services, ROS publishers and ROS subscribers
Supports all standard messages and is extendable
Generic (e.g. easy to change program from communicating with the simulation to communicating with a real robot)
I successfully compiled it with ROS Kinetic in ubuntu 16.04

## Slide 34: Control Mechanisms
C/ C++ API Ca lls
Cascaded Child script execution
LUA API calls
Custom LUA API callbacks
V-REP event callbacks
remote API function ca lls
ROS transit
custom communica tion
  s ocket, s erial, pipes , etc.
Add-on calls to LUA API
Script ca llba ck ca lls

## Slide 35: Control Mechanisms
If in doubt, use their website!
http:/ / www.coppeliarobotics .com

## Slide 36: Other features - Custom User Interfaces (QT-Based)

## Slide 37: Other features - Mesh Edit Modes
Triangle, vertex or edge edit mode
Modify meshes (adjust vertices, add/ remove triangles)
Semi-automatic prim itive shape extraction function
Triangle, vertex or edge extra ction
Mesh decomposition
Convex decomposition
Convex hull extraction
Mesh decim ation

## Slide 38: Other features
Headles s mode support (i.e. via command line)
Import formats: OBJ , STL, 3DS, DXF, COLLADA & URDF
Model browser and scene hierarchy
Multilevel undo / redo
Movie recorder (w. ray tracing)
Sim ula tion of pa int or welding seams
Static & dynamic textures
Exhaustive documentation
Etc.

## Slide 39: V-REP Source Code Licens ing

## Slide 40: Res ources
V-REP webs ite: www.coppeliarobotics .com
V-REP us er manual: www.coppeliarobotics .com/ helpFiles / V-REP forum: www.forum.coppeliarobotics .com
V-REP YouTube channel: VirtualRobotPlatform V-REP Twitter account: coppelia Robotic

## Slide 41: Starting your own project in GoRobots

## Slide 42: Starting your own project in GoRobots
1. As k for membership in ENS group on GitLa b (Koh, J an-Matthias, or Me)

## Slide 43: Starting your own project in GoRobots
As k for membership in ENS group on GitLa b (Koh, J an-Matthias, or Me)
Fork your version of GoRobots
Press this

## Slide 44: If you forked later than 08.47 this morning do this!
Configure a remote that points to the upstream repository in Git
$ git remote add upstream git@gitlab.com:ens_sdu/ gorobots.git
Fetch the branches and their respective commits from the upstream repository
$ git fetch upstream
Check out your fork's local master branch.
$ git checkout master
Merge the changes from upstream/ master into your local master branch (Sync.)
$ git merge upstream/ master
Check for merge conflicts with (you may need to ins tall meld)
$ meld .
No Important Changes (Check with meld)? → $ git reset --hard

## Slide 45: Starting your own project in GoRobots
As k for membership in ENS group on GitLa b (Koh, J an-Matthias, or Me)
Fork your version of GoRobots
Clone your fork to your Pc
git clone “this address”

## Slide 46: Starting your own project in GoRobots
As k for membership in ENS group on GitLa b (Koh, J an-Matthias, or Me)
Fork your version of GoRobots
Clone your fork to your Pc
Get pendulum s imula tion up and running by following the guide in the readme file
Please write me on mathias@mmmi.sdu.dk if you find any errors in the guide

## Slide 47: Starting your own project in GoRobots
1. As k for membership in ENS group on GitLa b (Koh, J an-Matthias, or Me)
Fork your version of GoRobots
Clone your fork to your Pc
Get pendulum s imula tion up and running by following the guide in the readme file
5. Start your own project and use the following s tructure
Your controller here →
e.g. /controllers/pendulum/pendulumController.cpp
Your makelistcatkin and child script here →
e.g. /projects/pendulum/catkin_ws/src/...
Your v-rep sim (.ttt) in v-rep_simulations in here →
e.g. /utils/v-rep_simulations/pendulum/ pendulum.ttt

## Slide 48: Starting your own project in GoRobots
As k for membership in ENS group on GitLa b (Koh, J an-Matthias, or Me)
Fork your version of GoRobots
Clone your fork to your Pc
Get pendulum s imula tion up and running by following the guide in the readme file
Start your own project and use the following s tructure
End your project with a merge request
Press this

## Slide 49: Questions and Getting started
Any Ques tion?
Try getting the pendulum s im ula tion to run on your PC!

## Slide 50: Installing VORTEX Physical engine
Go to: https :/ / www.cm -labs .com/ licens es /
Create free account
Go to: My Account > Downloa ds (the download page)
Pres s : Optiona l Downloa d > Vortex Studio (Linux)
Then go to: My Account > Licens es
  Then reques t a licens e for Vortex Studio Es s entials
Extract the downloaded folder
  Go to “Vortex_Studio…/ bin” (in the term ina l)
  Then run “./ VortexLicens e Manager --a ctiva te KEY”
Res tart V-REP

## Slide 51: V-REP Overview
What is it?
What can it do ?
Typical applications ?
General purpose robot s im ula tor with integra ted developm ent environment
Sensors, mechanisms, robots and whole s ys tems can be modelled and s im ula ted in various ways
Fast prototyping and verifica tion Controller development
Hardware control
Simulation of factory automation systems Safety monitoring
Product presentation etc.